## Slide 1
Team Details
  Team name: Ordinal
  Team leader name: Mehul Arora (with Jayadratha)
  Problem Statement: AI data halls need power and liquid cooling designed together, around equipment that can actually ship, by senior engineers in short supply. And only 6% of engineers trust AI results without checking.¹
Kirchhoff
by Ordinal
AI designs.
Physics checks.
An engineer signs.
¹ Omni Calculator, AI adoption in engineering.
Notes: We are Ordinal: Mehul Arora, who leads, and Jayadratha. Our product is Kirchhoff.
The problem has three parts. First, AI halls couple two disciplines that are usually designed apart: the electrical chain and the liquid-cooling loop. Racks now run far denser than older halls; Vertiv's own reference designs span 20 to 142 kW per rack.² Our sample hall runs 132 kW per rack. Second, the supply chain now shapes the design. Transformer lead times are long enough that Hitachi's standardisation push talks about getting them down to "as little as 12 months".³ A design that specifies equipment nobody can deliver is a design you redo. Third, the people who do this work are scarce, and Hitachi's HMAX Energy launch names workforce shortages directly.⁴
AI can draft, but engineers don't trust it, and they are right not to. Only 6% trust AI results without verification and 89% check by hand.¹ When six AI models were asked for one pump station's heating load, they answered anywhere from 25 to 150 MBH.⁵ A general-purpose model reported a voltage drop as 5% when it was 1.76%.⁶ The question has moved from "Should I use AI?" to "How do we control it?"⁷

## Slide 2
Brief about the idea
Start with a tender.
Finish with a signed design.
Gemini agents design power and liquid cooling for AI data halls.
A deterministic checker proves every number against cited clauses.
ERP lead times shape the equipment.
An engineer signs off.
Kirchhoff AI designs. Physics checks. An engineer signs.
SCREENSHOT shots/s03-workspace-signed.png
Workspace, Hall A (signed). 3D hall all green; agent lanes on the left all ✓; co-pilot on the right; revision bar reads "r1 (2 fail) → r2 ✓ → signed by Priya Raman (Reviewer)".
Demo: Priya Raman and all companies, people and data are fictional. IEC-based, illustrative values, not for construction.
Notes: Kirchhoff turns weeks of scarce senior-engineer work into one reviewed, signed design session.
Meet Priya, our persona: lead electrical engineer at a data-centre EPC contractor, with a small team and several hall packages due this month. Today she drafts. With Kirchhoff she reviews.
Here is the flow. Gemini agents read the tender, cite every requirement, and flag where the client contradicts itself. They lay out 48 racks of 132 kW in a 60 × 36 m hall, then design the 2N power chain and the liquid-cooling loop together. Procurement reads the ERP, and when a transformer can't ship in time, the engine swaps it for one that can. A deterministic checker, with no LLM in the verdict path, runs the clause-cited rule pack. The agents fix what fails, and the engineer signs. Approval raises purchase requisitions in the ERP and moves the deal in the CRM.
This maps onto the theme. Knowledge: every number links to its tender sentence and its clause. Collaboration: humans and agents share one workspace. Decisions: costed options and what-ifs come before you commit. Workflow: the path runs from tender PDF to signed revision to purchase requisitions to the CRM update. In short, one senior engineer supervises a team of design agents.

## Slide 3
Opportunities
How different is it from any of the other existing ideas?
Endra, ArchiLabs and Augmenta generate designs. None publicly shows an independent clause-cited checker, coupled power and liquid cooling, or ERP lead-time-aware design.
How will it be able to solve the problem?
Agents draft.
Physics verifies.
Engineers review.
USP of the proposed solution
AI designs.
Physics checks.
An engineer signs.
Kirchhoff
Endra Power Studio
ArchiLabs
Augmenta
ETAP 2026 Copilot
Independent checker, clause-cited findings
not shown (generic flags)
not shown
not shown
not shown
Power + liquid cooling in one model
not shown
not shown
not shown
not shown
ERP lead time as a checked rule
not shown
not shown
not shown
not shown
Data-centre power design
2N, DR, block (spec)
not shown
layouts + SLDs
conduit routing
studies from chat
Where it runs
browser
browser
browser
inside Revit
desktop
Based on public demos and material reviewed 13 Oct 2026.
Notes: The market is moving fast. Endra raised $50M in June 2026, and the press framed the round as data-centre design automation.⁸ Its Power Studio circuits a whole building in about a second (spec, from the team's competitor research). Yet its violation flags are generic, it cites no clauses, it checks itself, and no Endra demo shows busways, CDUs or 2N topologies. ArchiLabs pairs web CAD and agentic chat with data-centre layouts and SLDs, but no public video shows calculation depth.⁹ Augmenta routes conduit, and data centres are its most common project type, but runs take 26 minutes to 12 hours and it doesn't cite the code.¹⁰ ETAP's 2026 copilot runs studies from chat inside a dense desktop app.¹¹
We compete on three things nobody shows publicly:
1. An independent checker that cites clauses. The checker is deterministic code, separate from the agents that design, so the AI can't mark its own homework. Every finding carries its rule, its tender clause, its formula and inputs, and its value against its limit.
2. Power and cooling in one model. The checker catches coolant piping routed above a live busway feeder, a clash no single-discipline tool sees.
3. Design around what can ship. Lead time is a checked rule (R15) fed by ERP data. Speed-to-power needs speed-to-design.

## Slide 4
List of features offered by the solution
Tender intake with verified quotes
shots/s05-1-intake-quotes.png
Intake lane, "✓ quote verified" cards
Power and liquid cooling, one model
shots/s05-2-hall-3d-tiers.png
3D hall, busways and pipes on their tiers
Clause-cited checker: R01–R15, R04b
shots/s05-3-compliance-matrix.png
compliance matrix
ERP lead-time-aware redesign
shots/s05-4-option-r15-swap.png
option card showing the R15 swap
What-if impact chains
shots/s05-5-impact-chain.png
impact chain lit in two colours
Live voice co-pilot
shots/s05-6-copilot-voice.png
co-pilot voice button with on-screen transcript
Review and sign-off with revision hash
shots/s05-7-review-stamp.png
review stamp with hash
ERP and CRM handoff
shots/s05-8-integrations.png
Integrations page
Grid and Solar asset packs
shots/s05-9-solar-field.png
Solar field layout
All companies, people and data shown are fictional. IEC-based, illustrative values, not for construction.
Notes: - Intake. Gemini reads the tender PDF natively. A requirement is accepted only if pdfplumber finds its quote on the cited page. Intake also flags contradictions, such as §4.2 "2N" against Appendix B "block or distributed redundancy acceptable". Gemini reads the drawing, and the engine cross-checks it against the DXF.
- Gates and autonomy. Each run passes three gates: plan, option and review (spec). In Ask mode the engineer decides at every gate. In Auto, the tender's main clauses decide, but the review gate always waits for a human.
- Design. Layout places racks. Power offers three costed topologies: 2N, distributed redundant and block redundant (spec). Cooling sizes CDUs, hydraulic zones and pipes. In the sample hall, the 2N transformers run at 47.97% normal and 95.95% in N-1, against R01's limits of 80% normal and 100% N-1 (spec, tender §4.3). The design uses 9 CDUs of 1.2 MW.
- Checker. The checker runs the R01–R15 and R04b rule pack. Each finding shows its rule, clause chip, tender chip, formula, and a value-against-limit bar. The engine offers a fix only after re-running the full rule pack on it, and the owning agent then chooses on cost and margin.
- Lead-time redesign. The ERP shows the 2.5 MVA transformer with 0 in stock and a 98-week lead time, against the tender's 26-week limit. The engine swaps to a 3.15 MVA unit, with 6 in stock, and re-checks the fault level.
- What-if. Change rack kW, liquid fraction, the ΔV limit or the loading cap. The engine reruns every rule without saving and draws the impact chain across both disciplines.
- Voice. Gemini Live can call what_if, explain_finding and focus_element. If Live can't connect, push-to-talk takes over.
- Review. The review page shows the diff, the assumptions ledger (including what we don't check), and the findings summary. Approval stamps name, role, time and revision hash.
- Handoff. Approval raises purchase requisitions in the ERP sandbox, re-checks that SLD, BOQ and PR lines agree (R12), and moves the CRM opportunity. Exports cover a PDF calc report and a BOQ CSV.
- Asset packs. The Grid pack covers a 132 kV line. The Solar pack lays out a PV field. Both reuse the same shell and checker.

## Slide 5
Process flow diagram or Use-case diagram
Four phases. Three gates. One signed revision. (spec)
In Ask mode, the engineer decides at every gate. In Auto, the tender's own clauses decide. Sign-off always waits for a human.
Engineer
Gemini
agents (ADK)
Deterministic
engine + checker
(no LLM)
ERP / CRM
sandbox
P1
Intake and Orchestrator
P2
Design
P3
Route and check
P4
Handoff
Tender PDF
+ hall DXF
Intake + Orchestrator
verified quotes,
contradictions
Layout, then
Power ∥ Cooling
Procurement reads
ERP lead times
Engine swap +
Power re-check
ERP lead times
Route busways
and pipes
BOQ · Checker
(no LLM)
R12 re-check
PRs to ERP · CRM
stage update · audit
Plan gate
engineer
Option gate
engineer
Review gate
always human
fix loop
Notes: A run has four phases (spec).
1. P1: Intake and Orchestrator. Agents extract requirements and open questions. At the plan gate the engineer approves the plan, or Auto resolves it: a numbered clause beats an appendix, so the run proceeds as 2N.
2. P2: design. Layout places the racks. Power and Cooling then work in parallel. Procurement annotates the options with ERP lead times and applies the deterministic in-stock swap, and Power re-checks the fault level. At the option gate the engineer picks a topology.
3. P3: route and check. Layout routes the busways and Cooling routes the pipes. The engine derives the BOQ and draft PR lines, and the checker runs. The owning agents fix what fails, for at most 2 iterations (spec), and the checker re-runs after each. The run stops at the review gate, which is always human.
4. P4: handoff. On approval, PRs go to the ERP, R12 re-checks them against the SLD and BOQ, the CRM stage moves, and an audit entry is written.
Each phase runs in the background on Cloud Run and streams through Firestore, so you watch the agents work live.

## Slide 6
Wireframes/Mock diagrams of the proposed solution (optional)
Trust, built into the screen.
Every number comes from the engine.
Every requirement quote is found on its PDF page.
AI text can't carry its own digits.
Every sign-off stamps a revision hash.
WORKSPACE WIREFRAME · SPEC §12
Project
Ask | Auto
Request sign-off
Agent lanes
Intake
Layout
Power
Cooling
3D
SLD
Matrix
Options
Docs
Co-pilot
r1
r2
signed
FINDING DRAWER · ANNOTATED
1
Rule id
2
Clause chip and tender chip
3
Formula with inputs
4
Value-against-limit bar
5
Chosen fix and rejected alternative with deltas
6
"show on canvas"
SCREENSHOT shots/s07-finding-drawer-r05.png
Finding drawer open on R05 for FA-01: 82 m feeder, ΔV 2.16% against the 2.0% limit, §4.6 chip; fix options "2,000 A busway · 1.66% · +$11,480" and "parallel cable · 0.84% · +$15,580".
IEC-based, illustrative values, not for construction. Demo data is fictional.
Notes: This slide shows our trust model as the engineer sees it.
- Numbers. Every number on screen comes from the engine, which is pure Python with no LLM calls.
- Citations. Gemini returns a page, a verbatim quote and a value. We accept the requirement only if pdfplumber finds that quote on that page and the quote contains the value. Clicking the chip opens the PDF at the highlighted box.
- Digit filter. LLM text may contain digits only through placeholders that the engine fills, or through allowlisted ids such as FA-01, R11, §4.6 or 2N. Any other digit replaces the sentence with a template. A model can't invent a number on our screen.
- Ledger. Agents log the assumptions they make, and the ledger also lists what v0.1 does not check: earth-fault loop impedance, selectivity, arc flash and harmonics, for example.
- Accountability. An agent can't be held accountable, so only the engineer approves, and the stamp records name, role, time and the SHA-256 revision hash.

## Slide 7
Architecture diagram of the proposed solution
Gemini proposes. The engine decides.
ADK agents run on Cloud Run with Gemini 3.8 Flash. The engine and checker are plain Python with no LLM. Firestore streams every step live; Firebase serves, signs in and attests.
Browser
React 19 on Firebase Hosting
Workspace
React Flow + ELK SLD,
react-three-fiber 3D hall
Static demo world JSON
Firebase Auth (anonymous)
Firebase App Check
Gemini Live native
audio (us-central1)
voice via Firebase AI Logic
Cloud Run: kirchhoff-api (public)
FastAPI
ID token + App Check + ownership
ADK 2.x agents (LlmAgent + function tools)
Intake, Orchestrator, Layout, Power,
Cooling, Procurement, Docs, Co-pilot, Asset
No LLM in the verdict path
kirchhoff_engine
pandapower,
shapely, ezdxf
Checker
rule pack
R01–R15 + R04b
Firestore
Cloud Run:
kirchhoff-enterprise
(private)
ERP + CRM sandbox
runs, leases, events
Google ID token
/api rewrite
onSnapshot,
read-only
Cloud Storage
signed URLs
Gemini 3.8 Flash
on Vertex AI (global)
structured output,
function calls
Cloud Build
one image
Notes: Read it left to right.
- Browser. A React 19 app runs on Firebase Hosting. The demo world is static JSON, so browsing works even with the backend down. Anonymous Firebase Auth gives each visitor a private workspace, and App Check attests the app. The client reads Firestore through live listeners and never writes to it. Voice goes through Firebase AI Logic to the Gemini Live native-audio model in us-central1, and its tool calls come back to our API.
- kirchhoff-api on Cloud Run (public, behind the Hosting rewrite). FastAPI verifies the Firebase ID token, the App Check token and workspace ownership on every call. ADK 2.x agents (LlmAgent + function tools) run on Gemini 3.8 Flash through Vertex AI (global), with structured outputs and function calling. The tools call kirchhoff_engine, which uses pandapower for IEC 60909 short circuit, shapely for geometry and ezdxf for drawings, plus the rule pack. That box is the trust boundary: no LLM inside.
- Firestore holds run state, leases, the live event stream, revisions, findings, approvals and the sandbox seed. Cloud Storage holds tenders, drawings and exports, served through signed URLs.
- kirchhoff-enterprise on Cloud Run (private). The ERP and CRM sandbox runs from the same image. Only our dedicated, least-privilege service account can invoke it, using a Google ID token.
- Cloud Build builds one image that deploys as both services.
We chose Cloud Run over a managed agent runtime because the engine needs native scientific Python and runs execute as long background phases.

## Slide 8
Technologies to be used in the solution
AI
Gemini 3.8 Flash on Vertex AI
Gemini Live
Google ADK 2.x
GOOGLE CLOUD
Cloud Run
Firestore
Cloud Storage
Cloud Build
FIREBASE
Hosting
Auth
App Check
AI Logic
ENGINE
FastAPI
pandapower
shapely
ezdxf
INTERFACE
React 19
React Flow + ELK
react-three-fiber
Notes: Every Google service in this list carries load.
- Gemini does the reading, the citations, the planning, the choices with reasons, the explanations and the voice.
- ADK agents call engine tools; the run orchestrator orders the phases, the gates and the fix loop.
- Cloud Run hosts the agent and engine API and the private enterprise sandbox.
- Firestore is the live event bus and the audit trail.
- Firebase serves the app, gives every visitor an anonymous workspace, attests requests with App Check, and connects the browser to Gemini Live.
The engine stands on open-source physics. pandapower runs IEC 60909 short circuit, shapely handles clash and clearance geometry, ezdxf reads the hall DXF, and pdfplumber verifies quotes. The interface uses React Flow with ELK layout for the single-line diagram and react-three-fiber for the 3D hall.

## Slide 9
Estimated implementation cost (optional)
Run cost
1 warm Cloud Run instance (spec)
USD 200 budget with alerts (spec)
Gemini 3.8 Flash: $0.75 / $3.75 per 1M tokens¹²
Per design: ~$0.057 (measured on a live run, 15 Oct 2026)
How we charge
Seats for design teams; enterprise tier adds ERP/CRM connectors.
ENTERPRISE INTEGRATION
Kirchhoff
/api/enterprise
ERP (SAP-style)
CRM (Salesforce-style)
sandbox (simulated) today; real connectors on the roadmap
¹² Gemini API pricing: $0.75 in / $3.75 out per million tokens through 31 Dec 2026, doubling from 1 Jan 2027.
Notes: Cost. The prototype runs on one warm API instance with no CPU throttling, scaling to a maximum of 3 (spec). The enterprise sandbox is a second small service. Gemini 3.8 Flash costs $0.75 per million input tokens and $3.75 per million output tokens through 31 December 2026, and the price doubles from 1 January 2027.¹² The engine does the heavy work without tokens. A what-if runs in about 8 ms and makes no LLM call. Budget alerts fire at 50% and 90% (spec). Measured on a live run, 15 Oct 2026: a full P1→P4 run on Vertex AI took 176.5 s and used 10,432 input tokens and 12,991 output tokens, about $0.057 per design at $0.75 per million input and $3.75 per million output tokens. The golden capture may replace this figure.
Business model (proposed). We sell to data-centre EPC contractors and design consultancies, where the buyer is the engineering lead whose senior hours are the bottleneck. Design teams pay per seat. The enterprise tier adds real ERP and CRM connectors on the same API contract our sandbox uses today, and later an on-prem model option. We start with design partners before setting public prices.
Enterprise integration. Kirchhoff already talks to an ERP and a CRM through APIs: a separate private Cloud Run service seeded with 60 materials, 9 CRM opportunities and 3 historical PRs. Approval raises purchase requisitions, re-checks them against the SLD and BOQ, and moves the opportunity to "Design approved". Swapping the sandbox for SAP or Salesforce changes the adapter, not the workflow.

## Slide 10
Snapshots of the prototype
SCREENSHOT shots/s11-1-projects-dashboard.png
Projects dashboard. Hall A "Signed", Hall B "Not started", Grid and Solar cards; fictional-data banner visible.
1
Your firm's projects, already in motion
SCREENSHOT shots/s11-2-hall-b-live-run.png
Workspace during the Hall B live run. Power and Cooling lanes both active; elapsed-time clock; SLD staging in.
2
Agents design in parallel
SCREENSHOT shots/s11-3-finding-drawer-r11.png
3D hall, R11 finding drawer open. H-Z2 red where it crosses FB-03; §6.3.4 clause chip; both fix options with cost deltas.
3
Every finding cites its clause
SCREENSHOT shots/s11-4-options-r15-swap.png
Options tab, 2N card. "2.5 MVA · stock 0 · 98 wk > 26 wk (§2.3)" struck through; "3.15 MVA · stock 6 · 38.07% / 76.15%"; fault level 65.42 kA.
4
98 weeks → ships from stock
SCREENSHOT shots/s11-5-what-if-200kw.png
What-if at 200 kW per rack. Impact chain lit rack → busway → board → transformer (power colour) and rack → zone → CDU (cooling colour); counters "60 findings · 18 impact chains".
5
200 kW per rack: 18 impact chains
SCREENSHOT shots/s11-6-review-approved.png
Review page after approval. Diff, ledger with its "not checked" list, stamp "You (Demo Reviewer) · time · revision hash".
6
Signed, with a revision hash
All companies, people and data shown are fictional. IEC-based, illustrative values, not for construction.
Notes: These come from the live product at kirchhoff.web.app. Every company and person in the demo world is fictional.
1. The projects dashboard for Meridian Power Engineering, a fictional EPC firm, with data-hall, grid and solar projects in different states.
2. Agent lanes during a live Hall B run. The footage is time-compressed and carries an elapsed-time clock.
3. The finding drawer for R11. Header H-Z2 runs above feeder FB-03 at y ≈ 24 m, breaking tender §6.3.4. The engine offers two verified fixes: a local drop (+$420, 1 pipe changed) or a reroute (−$910, 2 pipes changed).
4. Option cards after the R15 swap. The 2.5 MVA unit has 0 in stock and a 98-week lead time, so the engine picks the 3.15 MVA unit, with 6 in stock, which runs at 38.07% normal and 76.15% in N-1. The fault level moves from 60.45 to 65.42 kA and is re-checked.
5. The what-if at 200 kW per rack. R01 fails at 113.6%, R02 at 2,343 A, and R08 at 2,560 kW against 2,400 kW; R03, R05, R07 and R09 also fail. That is 60 findings in 18 impact chains.
6. The review page with the diff, the assumptions ledger and the approval stamp.

## Slide 11
Prototype Performance report/Benchmarking
35/35
seeded design faults caught, 0 false positives
149
first-pass checks: 147 pass, 2 fail, both fixed
~8 ms
per what-if after warm-up
Byte-identical
output across Python hash seeds
SCREENSHOT shots/s12-compliance-matrix-first-pass.png
Compliance matrix at the end of the first pass. Counter "149 checks · 147 pass · 2 fail" with the two red cells (R05 FA-01, R11 H-Z2).
ESTIMATE
~10 engineer-hours
saved per change iteration (basis in notes)
IEC-based, illustrative values, not for construction.
Notes: What we measured on 14 Oct.
- Checker benchmark. We seeded 35 mutations into the design, covering the rule pack. The checker caught all 35, with zero false positives.
- First pass on the golden 2N design. It produced 149 findings: 147 pass and 2 fail. Feeder FA-01 (82 m) drops 2.16% against the 2.0% limit (R05). The fixes are a 2,000 A busway (1.66%, +$11,480) or a parallel cable (0.84%, +$15,580). Header H-Z2 runs above FB-03 (R11). The fixes are a local drop (+$420) or a reroute (−$910).
- What-if at 200 kW per rack. Seven rules fail, producing 60 findings in 18 impact chains, in about 8 ms after warm-up.
- Determinism. Output is byte-identical across Python hash seeds, so the same design always gives the same verdict.
- Business result in the sandbox. A 98-week transformer becomes a 3.15 MVA unit shipped from stock, at 38.07% / 76.15% loading.
Impact estimate, labelled as an estimate. We estimate about 10 engineer-hours saved per design-change iteration. The basis is the industry's own figure for reworking a design change by hand: "10+ hours", from Endra's September 2026 launch demo.¹³ That figure is unaudited and comes from commercial buildings.¹⁴ Kirchhoff re-checks every rule in milliseconds, and the engineer's time goes to review rather than recalculation. The spec's first-design baseline is 4–8 weeks for a first coordinated electrical package (spec; [TBD: source citation]). Kirchhoff produces a checked concept design, not construction drawings, so the honest comparison is first checked concept against first concept. [TBD: measured time from upload to a checker-clean revision, median of 5 live runs, excluding time at human gates (spec §4, metric 1).] Measured on a live intake run on Vertex AI, 15 Oct 2026: requirement recall 0.84 against our hand-labelled ground truth for the Hall A tender, with 27 of 28 extracted quotes verified word for word against the tender PDF; the one unverified quote was shown as unverified, never as fact.

## Slide 12
Additional Details/Future Development (if any)
Now
AI data hall, plus thin Grid (132 kV line) and Solar packs on the same engine.
Next
Real SAP and Salesforce connectors, Revit/IFC round-trip, PLM, 800 VDC architectures, on-prem Gemma.
Smart engineering
One thread from tender to procurement.
SCREENSHOT shots/s13-grid-pack.png
Grid pack. 132 kV line on the static map, conductor comparison cards, mini SLD.
SCREENSHOT shots/s13-solar-pack.png
Solar pack. Field layout with tables; card "STR-28 recommended · 327 tables · ~5,036 kWp · DC/AC 1.26 · clear-sky yield ~2,639 kWh/kWp (clear-sky only)".
IEC-based, illustrative values, not for construction. Demo data is fictional.
Notes: Asset packs today. Both packs reuse the shell, the checker and the finding drawer, run by one Asset agent.
- Grid. A 132 kV double-circuit line of about 18 km (spec) to the campus substation. It compares three ACSR conductors (spec) on ampacity, voltage regulation and I²R losses, and computes the fault level at the connection.
- Solar. A ground-mount field next to the hall. The engine recommends string option STR-28: 327 tables, about 5,036 kWp, DC/AC ratio 1.26. Its clear-sky yield is about 2,639 kWh/kWp, a clear-sky figure only, with no weather losses.
Roadmap. We cut these from the hackathon build, and they come next: real ERP and CRM connectors, Revit/IFC round-trip, PLM integration, 800 VDC architectures, auto-layout from messy drawings, Gemma on-prem, live multi-user presence, and drawing render review.
Smart engineering (Hitachi-relevant). Hitachi's Smart Engineering track asks for solutions that "connect engineering data across the product lifecycle, automate the processing of legacy documents and requirements, and speed up design with AI agents".¹⁵ Kirchhoff already links tender clauses to design, checks, purchase requisitions and CRM in one audited thread. Hitachi Energy is designing an 800 VDC grid-to-rack system with NVIDIA.¹⁶ An 800 VDC topology pack and the Grid pack extend that thread from the substation to the rack.

## Slide 13
Provide links to your:
GitHub Public Repository
https://github.com/mehular0ra/kirchhoff
Demo Video Link (3 Minutes)
[TBD: video URL]
(runs 2:45)
QR appears
when the
URL is filled
Final Product Link
https://kirchhoff.web.app
(no login: "Enter the demo workspace" opens the guided tour)
Notes: The live URL opens on a landing page with one primary button. The welcome screen offers a short guided tour. To see a live run, open Hall B and choose "Run it live", or replay a recorded run. The repository README has the architecture, the trust model and the local quick start.

## Slide 14
Team Ordinal
Mehul Arora
Team lead. AI engineer · built Kirchhoff's agents, engine and app; builds production multi-agent systems on Gemini and Google ADK; MS by Research in ML, IIIT Hyderabad
Jayadratha
Graph ML researcher · built the bids inbox, asset agent and test suite, ran cloud and the golden capture; previously at Vikram Solar
Built in JAPAC, for engineering teams everywhere.
THEME
Future of Work & Enterprise Productivity
Notes: Mehul Arora built Kirchhoff's agent layer, its deterministic engine and the web app. He builds production multi-agent LLM systems on Gemini, Google ADK and Cloud Run, and earlier did graph neural network research for his MS by Research at IIIT Hyderabad and data science on US power-market datasets. Jayadratha Gayen built the bids inbox, the asset agent and the end-to-end test suite, and ran Kirchhoff's cloud deployments and golden capture. He is a graph neural networks researcher and previously worked at Vikram Solar, bringing solar and energy-sector experience. We built Kirchhoff from scratch during the hackathon window, on Google Cloud end to end.

## Slide 15
Kirchhoff by Ordinal
AI designs. Physics checks. An engineer signs.
kirchhoff.web.app
Notes: Thank you. Try it at kirchhoff.web.app; there's no login, and a guided tour walks you through it.